## Slide 1: 國立金門大學 智慧物聯網實務與應用 Ameba_進階程式設計 (類比讀寫)
講師：曹永忠
國立金門大學-工業工程與管理學系
日期：106年6月24~25日

## Slide 2: Arduino 程式介紹

## Slide 3: Arduino 程式架構
3
2017/6/24

## Slide 4: Arduino程式的介面
功能表

## Slide 5
同等於C語言的Rebuild All
將程式燒入到
Arduino
開新檔案
開啟舊檔
儲存檔案
回傳值

## Slide 6
撰寫程式內容
要注意是否連線，
若未連線可以Rebuild但不可燒入

## Slide 7
未連線
已連線

## Slide 8: Arduino程式架構
(一.)宣告:
Arduino宣告方式與C相同,例如:int，float…
(二.)初始化 Setup():
使Arduino板子裝置妥當的指令
EX:
int ledPin=7; / 宣告Arduino7號腳為輸入腳/
Setup()
{
pinMode(ledPin,INPUT);
}

## Slide 9
(三.)執行Loop():
為程式的主要內容,這程式內容會一直重複被執行
EX:
Loop()
{
……
}

## Slide 10
(四.)函式:
1. pinMode(7,INPUT) //將腳位7設定為輸入模式
2. digitalWrite(8,HIGH) (數位腳專用)
//將腳位8設定輸出高電位
3. val=digitalRead(7) (數位腳專用)
//讀出腳位7的值並指定給 val變數

## Slide 11
4.analogWrite(9,128) (數位訊號專用所設計的函式)
//將擁有PWM的數位腳位9 設定輸出電位2.5V對應值大 約為128
5. val=analogRead(0) (類比腳專用) //讀出腳位0的值並指定給 val變數(且analogRead可讀 取範圍0(0V)~1023(5V))

## Slide 12: 系統開發
12
2017/6/24

## Slide 13: 啟動開發環境
13
2017/6/24

## Slide 14: 開啟程式
14
2017/6/24

## Slide 15: 啟動程式
15
2017/6/24

## Slide 16: 選擇開發版
16
2017/6/24

## Slide 17: 確定通訊埠
17
2017/6/24

## Slide 18: 選擇通訊埠
18
2017/6/24

## Slide 19: 開啟程式
19
2017/6/24

## Slide 20: Ameba 腳位說明
20
2017/6/24

## Slide 21
21
2017/6/24

## Slide 22: 簡單類比輸入模組
22
2017/6/24

## Slide 23: 類比搖桿元件
23
2017/6/24

## Slide 24: 類比搖桿元件
24
2017/6/24

## Slide 25: 類比搖桿連接電路
25
2017/6/24

## Slide 26: 類比資料輸入
26
2017/6/24

## Slide 27: 讀取搖桿資料
27
2017/6/24

## Slide 28: Joystick01
28
2017/6/24
#define VRX 1
#define VRY 2
設定類比輸入接腳
Notes: 設定類比輸入接腳

## Slide 29: Joystick02
29
2017/6/24
#define VRX 1
#define VRY 2
void setup() {
// put your setup code here, to run once:
Serial.begin(9600) ;
Serial.println("Program Start") ;
}
啟動監控通訊埠與通訊速度
Notes: 啟動監控通訊埠與通訊速度

## Slide 30: Joystick03
30
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
}
讀取類比輸入資料(X)
Notes: 讀取類比輸入資料

## Slide 31: Joystick04
31
2017/6/24
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
讀取類比輸入資料(Y)
Notes: 設定類比輸入接腳

## Slide 32: 看不到X值
32
2017/6/24
Notes: 設定類比輸入接腳

## Slide 33: 看不到X值
33
2017/6/24
Notes: 設定類比輸入接腳

## Slide 34: Joystick5
34
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}
加入延遲
Notes: 加入延遲

## Slide 35: 簡單PWM輸出
35
2017/6/24

## Slide 36: LED 元件
36
2017/6/24

## Slide 37: LED 元件
37
2017/6/24

## Slide 38: PWM連接電路
38
2017/6/24

## Slide 39: 類比資料輸出
39
2017/6/24

## Slide 40: 使用PWM驅動ＬＥＤ亮度
40
2017/6/24

## Slide 41: ＬＥＤ ＰＷＭ０１
41
2017/6/24
#define LED1 11
設定類比輸出接腳
Notes: 設定類比輸入接腳

## Slide 42: ＬＥＤ ＰＷＭ０２
42
2017/6/24
analogWrite(LED, 50) ;
delay(1000) ;
analogWrite(LED, 220) ;
delay(1000) ;
1.輸出微亮
2.等一秒
3.輸出高亮度
4.等一秒
5.重複
Notes: 啟動監控通訊埠與通訊速度

## Slide 43: ＬＥＤ ＰＷＭ０３
43
2017/6/24
#define LED1 11
int fadeValue = 0 ;
int fadeWay = 1 ;
void setup() {
analogWrite(LED1,fadeValue) ;
}
Notes: 讀取類比輸入資料

## Slide 44: ＬＥＤ ＰＷＭ０３
44
2017/6/24
void loop() {
if (fadeValue >255)
{
fadeValue = 0 ;
fadeWay = 1 ;
}
if (fadeValue < 0 )
{
fadeValue = 255 ;
fadeWay = -1 ;
}
analogWrite(LED1,fadeValue) ; // change PWM
fadeValue += fadeWay ;
delay(30) ;
}
Notes: 設定類比輸入接腳

## Slide 45: 簡單類比輸入與PWM輸出
45
2017/6/24

## Slide 46: 類比搖桿元件
46
2017/6/24

## Slide 47: LED 元件
47
2017/6/24

## Slide 48: 類比輸入與PWM輸出連接電路（兩路）
48
2017/6/24

## Slide 49: 兩路輸出控制兩路ＰＷＮ輸出
49
2017/6/24

## Slide 50: 使用PWM驅動ＬＥＤ亮度
50
2017/6/24

## Slide 51: Joystick_PWM01
51
2017/6/24
#define VRX A1
#define VRY A2
#define LED1 11
#define LED2 12
void setup() {
// put your setup code here, to run once:
Serial.begin(9600) ;
Serial.println("Program Start") ;
}
Notes: #define VRX A1
#define VRY A2
#define LED1 11
#define LED2 12
void setup() {
// put your setup code here, to run once:
Serial.begin(9600) ;
Serial.println("Program Start") ;
}
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 52: Joystick_PWM01
52
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}
Notes: #define VRX A1
#define VRY A2
#define LED1 11
#define LED2 12
void setup() {
// put your setup code here, to run once:
Serial.begin(9600) ;
Serial.println("Program Start") ;
}
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 53: Joystick_PWM02
53
2017/6/24
#define VRX A1
#define VRY A2
#define LED1 11
#define LED2 12
int rx = 0 ;
int ry = 0 ;
void setup() {
// put your setup code here, to run once:
Serial.begin(9600) ;
Serial.println("Program Start") ;
}
Notes: #define VRX A1
#define VRY A2
#define LED1 11
#define LED2 12
int rx = 0 ;
int ry = 0 ;
void setup() {
// put your setup code here, to run once:
Serial.begin(9600) ;
Serial.println("Program Start") ;
}
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 54: Joystick_PWM02
54
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}
Notes: #define VRX A1
#define VRY A2
#define LED1 11
#define LED2 12
int rx = 0 ;
int ry = 0 ;
void setup() {
// put your setup code here, to run once:
Serial.begin(9600) ;
Serial.println("Program Start") ;
}
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 55: Joystick_PWM03
55
2017/6/24
#define VRX A1
#define VRY A2
#define LED1 11
#define LED2 12
int rx = 0 ;
int ry = 0 ;
void setup() {
// put your setup code here, to run once:
Serial.begin(9600) ;
Serial.println("Program Start") ;
}
Notes: #define VRX A1
#define VRY A2
#define LED1 11
#define LED2 12
int rx = 0 ;
int ry = 0 ;
void setup() {
// put your setup code here, to run once:
Serial.begin(9600) ;
Serial.println("Program Start") ;
}
void loop() {
// put your main code here, to run repeatedly:
rx = analogRead(VRX) ;
ry = analogRead(VRY) ;
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 56: Joystick_PWM03
56
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
rx = analogRead(VRX) ;
ry = analogRead(VRY) ;
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}
Notes: #define VRX A1
#define VRY A2
#define LED1 11
#define LED2 12
int rx = 0 ;
int ry = 0 ;
void setup() {
// put your setup code here, to run once:
Serial.begin(9600) ;
Serial.println("Program Start") ;
}
void loop() {
// put your main code here, to run repeatedly:
rx = analogRead(VRX) ;
ry = analogRead(VRY) ;
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 57: Joystick_PWM01
57
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 58: Joystick_PWM01
58
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 59: Joystick_PWM01
59
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 60: Joystick_PWM01
60
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 61: Joystick_PWM01
61
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 62: Joystick_PWM01
62
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 63: Joystick_PWM01
63
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 64: Joystick_PWM01
64
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 65: Joystick_PWM01
65
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 66: Joystick_PWM01
66
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 67: Joystick_PWM01
67
2017/6/24
void loop() {
// put your main code here, to run repeatedly:
Serial.print("Read X is :(") ;
Serial.print(analogRead(VRX)) ;
Serial.print(") \n") ;
Serial.print("Read Y is :(") ;
Serial.print(analogRead(VRY)) ;
Serial.print(") \n") ;
delay(300) ;
}

## Slide 68: 如何視覺化
68
2017/6/24

## Slide 69: 使用Google Developer資源
69
2017/6/24

## Slide 70: 視覺化儀表板
70
2017/6/24

## Slide 71: 視覺化儀表板重點解說
71
2017/6/24
<html>
<head>
<script type="text/javascript" src="https://www.gstatic.com/charts/loader.js"></script>
<script type="text/javascript">
google.charts.load('current', {'packages':['gauge']});
google.charts.setOnLoadCallback(drawChart);
使用Google 資源
載入Google Chart 資源

## Slide 72: 視覺化儀表板重點解說
72
2017/6/24
function drawChart() {
var data = google.visualization.arrayToDataTable([
['Label', 'Value'],
['Brother', 68]
]);
[‘Label’, ‘Value’]資料標題
第二列的[‘Brother’, 68] 為資料第一筆，
前面為資料名稱，後面資料內容

## Slide 73: 視覺化儀表板重點解說
73
2017/6/24
var options = {
width: 800, height: 800,
redFrom: 80, redTo: 100,
yellowFrom:60, yellowTo: 80,
minorTicks: 5
};
width: ， height 為 每一個Chart的寬與高
redFrom: 紅色區域開始, redTo:紅色區域結束
yellowFrom:黃色區域開始, yellowTo:黃色區域結束
minorTicks: 5 最小刻度

## Slide 74: 視覺化儀表板重點解說
74
2017/6/24
var chart = new google.visualization.Gauge(document.getElementById('chart_div'));
chart.draw(data, options);
var chart = new google.visualization.Gauge(document.getElementById(‘chart_div’))產生儀表板
chart.draw(data, options);畫出儀表板

## Slide 75: 視覺化儀表板重點解說
75
2017/6/24
<body>
<div id="chart_div" style="width: 800px; height: 800px;"></div>
</body>
<div id=“chart_div” style=“width: 800px; height: 800px;”></div>產生叫” chart_div”的 繪圖空間
width: 800px 繪圖空間寬度
height: 800px;繪圖空間高度

## Slide 76: 視覺化儀表板 程式開發
76
2017/6/24

## Slide 77: 開啟程式DHT11_Pin7_WIFI_Server_Guage
77
2017/6/24

## Slide 78: DHT11_Pin7_WIFI_Server_Guage
78
2017/6/24
#include <WiFi.h>
// your network key Index number (needed only for WEP)
//-------------- dht use
#include "DHT.h"
#define DHTPIN 7 // what digital pin we're connected to
#define DHTTYPE DHT11 // DHT 11
Notes: #include <WiFi.h>
// your network key Index number (needed only for WEP)
//-------------- dht use
#include "DHT.h"
#define DHTPIN 7 // what digital pin we're connected to
#define DHTTYPE DHT11 // DHT 11
//#define DHTTYPE DHT22 // DHT 22 (AM2302), AM2321
//#define DHTTYPE DHT21 // DHT 21 (AM2301)
DHT dht(DHTPIN, DHTTYPE);
//----wifi use
uint8_t MacData[6];
char ssid[] = "BruceSonyC5"; // your network SSID (name)
char pass[] = "12345678"; // your network password
int keyIndex = 0;
IPAddress Meip , Megateway , Mesubnet ;
String MacAddress ;
int status = WL_IDLE_STATUS;
WiFiServer server(80);
//-----end of wifi use
void setup() /*----( SETUP: RUNS ONCE )----*/
{
Serial.begin(9600);
Serial.println("DHTxx test!");
dht.begin();
if (WiFi.status() == WL_NO_SHIELD) {
Serial.println("WiFi shield not present");
// don't continue:
while (true);
}
String fv = WiFi.firmwareVersion();
if (fv != "1.1.0") {
Serial.println("Please upgrade the firmware");
}
MacAddress = GetWifiMac() ; // get MacAddress
ShowMac() ; //Show Mac Address
// attempt to connect to Wifi network:
initializeWiFi();
server.begin();
// you're connected now, so print out the status:
ShowInternetStatus();
}// END Setup
static int count = 0;
void loop()
{
// Reading temperature or humidity takes about 250 milliseconds!
// Sensor readings may also be up to 2 seconds 'old' (its a very slow sensor)
float h = dht.readHumidity();
// Read temperature as Celsius (the default)
float t = dht.readTemperature();
// Read temperature as Fahrenheit (isFahrenheit = true)
float f = dht.readTemperature(true);
Serial.print("Humidity: ");
Serial.print(h);
Serial.print(" % and ");
Serial.print("Temperature: ");
Serial.print(t);
Serial.print(" *C ");
Serial.print(f);
Serial.print(" *F\t\n");
// wifi code here
// listen for incoming clients
WiFiClient client = server.available();
if (client)
{
Serial.println("Now Someone Access WebServer");
Serial.println("new client");
// an http request ends with a blank line
boolean currentLineIsBlank = true;
while (client.connected())
{
if (client.available())
{
char c = client.read();
Serial.write(c);
// if you've gotten to the end of the line (received a newline
// character) and the line is blank, the http request has ended,
// so you can send a reply
if (c == '\n' && currentLineIsBlank)
{
// send a standard http response header
client.println("HTTP/1.1 200 OK");
client.println("Content-Type: text/html");
client.println("Connection: close"); // the connection will be closed after completion of the response
client.println("Refresh: 5"); // refresh the page automatically every 5 sec
client.println();
client.println("<!DOCTYPE HTML>");
client.println("<html>");
// output the value of each analog input pin
client.println("<head>");
client.println("<script type='text/javascript' src='https://www.gstatic.com/charts/loader.js'></script>");
client.println("<script type='text/javascript'>");
client.println("google.charts.load('current', {'packages':['gauge']});");
client.println("google.charts.setOnLoadCallback(drawChart);");
client.println(" function drawChart() {");
client.println("var data = google.visualization.arrayToDataTable([['Label', 'Value'],['濕度',");
client.println(h);
client.println("],]);");
client.println(" var options = {width: 300, height: 300,redFrom: 90, redTo: 100,yellowFrom:75, yellowTo: 90,minorTicks: 5};");
client.println("var chart = new google.visualization.Gauge(document.getElementById('chart_div'));");
client.println("chart.draw(data, options);");
client.println("}");
client.println("</script>");
client.println("</head>");
client.println("<meta charset='utf-8'>");
client.println("<body>");
client.println("<div id='chart_div' style='width: 300px; height: 300px;'></div>");
client.println("</body>");
/*
client.print("Humidity: ");
client.print(h);
client.print(" % and ");
client.print("Temperature: ");
client.print(t);
client.print("*C and ");
client.print(f);
client.print("*F (end) ");
client.println("<br />");
*/
client.println("</html>");
break;
}
if (c == '\n')
{
// you're starting a new line
currentLineIsBlank = true;
} else if (c != '\r')
{
// you've gotten a character on the current line
currentLineIsBlank = false;
}
}
}
// give the web browser time to receive the data
delay(1);
// close the connection:
client.stop();
Serial.println("client disonnected");
}
delay(800) ;
} // END Loop
void ShowMac()
{
Serial.print("MAC:");
Serial.print(MacAddress);
Serial.print("\n");
}
String GetWifiMac()
{
String tt ;
String t1, t2, t3, t4, t5, t6 ;
WiFi.status(); //this method must be used for get MAC
WiFi.macAddress(MacData);
Serial.print("Mac:");
Serial.print(MacData[0], HEX) ;
Serial.print("/");
Serial.print(MacData[1], HEX) ;
Serial.print("/");
Serial.print(MacData[2], HEX) ;
Serial.print("/");
Serial.print(MacData[3], HEX) ;
Serial.print("/");
Serial.print(MacData[4], HEX) ;
Serial.print("/");
Serial.print(MacData[5], HEX) ;
Serial.print("~");
t1 = print2HEX((int)MacData[0]);
t2 = print2HEX((int)MacData[1]);
t3 = print2HEX((int)MacData[2]);
t4 = print2HEX((int)MacData[3]);
t5 = print2HEX((int)MacData[4]);
t6 = print2HEX((int)MacData[5]);
tt = (t1 + t2 + t3 + t4 + t5 + t6) ;
Serial.print(tt);
Serial.print("\n");
return tt ;
}
String print2HEX(int number) {
String ttt ;
if (number >= 0 && number < 16)
{
ttt = String("0") + String(number, HEX);
}
else
{
ttt = String(number, HEX);
}
return ttt ;
}
void printWifiData()
{
// print your WiFi shield's IP address:
Meip = WiFi.localIP();
Serial.print("IP Address: ");
Serial.println(Meip);
Serial.print("\n");
// print your MAC address:
byte mac[6];
WiFi.macAddress(mac);
Serial.print("MAC address: ");
Serial.print(mac[5], HEX);
Serial.print(":");
Serial.print(mac[4], HEX);
Serial.print(":");
Serial.print(mac[3], HEX);
Serial.print(":");
Serial.print(mac[2], HEX);
Serial.print(":");
Serial.print(mac[1], HEX);
Serial.print(":");
Serial.println(mac[0], HEX);
// print your subnet mask:
Mesubnet = WiFi.subnetMask();
Serial.print("NetMask: ");
Serial.println(Mesubnet);
// print your gateway address:
Megateway = WiFi.gatewayIP();
Serial.print("Gateway: ");
Serial.println(Megateway);
}
void ShowInternetStatus()
{
if (WiFi.status())
{
Meip = WiFi.localIP();
Serial.print("Get IP is:");
Serial.print(Meip);
Serial.print("\n");
}
else
{
Serial.print("DisConnected:");
Serial.print("\n");
}
}
void initializeWiFi() {
while (status != WL_CONNECTED) {
Serial.print("Attempting to connect to SSID: ");
Serial.println(ssid);
// Connect to WPA/WPA2 network. Change this line if using open or WEP network:
status = WiFi.begin(ssid, pass);
// status = WiFi.begin(ssid);
// wait 10 seconds for connection:
delay(10000);
}
Serial.print("\n Success to connect AP:") ;
Serial.print(ssid) ;
Serial.print("\n") ;
}

## Slide 79: DHT11_Pin7_WIFI_Server_Guage監控畫面
79
2017/6/24

## Slide 80: 使用瀏覽器進入系統
80
2017/6/24
1.先使用筆電或手機，使用wifi，並將ＷＩＦＩ熱點連接到與Ameba相同的熱點
2.進入瀏覽器(建議使用chrome)
3.網址列輸入上面IP(本例子為：http://192.168.43.150/

## Slide 81: DHT11_Pin7_WIFI_Server_Guage網頁畫面
81
2017/6/24

## Slide 82: 自我練習
82
2017/6/24

## Slide 83: 習題
83
2017/6/24
請將溫度、濕度的數值都讀出來
溫度顯示在一個Gauge 抬頭設為:SOUND”
黃色區域為55-80
紅色區域為80-100

## Slide 84: Q & A
感謝聆聽
恭請指教

## Slide 85: 練習解答
85
2017/6/24

## Slide 86: 開啟程式DHT11_Pin7_WIFI_Server_TwoGuage
86
2017/6/24

## Slide 87: DHT11_Pin7_WIFI_Server_TwoGuage
87
2017/6/24
#include <WiFi.h>
// your network key Index number (needed only for WEP)
//-------------- dht use
#include "DHT.h"
#define DHTPIN 7 // what digital pin we're connected to
#define DHTTYPE DHT11 // DHT 11
//#define DHTTYPE DHT22 // DHT 22 (AM2302), AM2321
//#define DHTTYPE DHT21 // DHT 21 (AM2301)
Notes: #include <WiFi.h>
// your network key Index number (needed only for WEP)
//-------------- dht use
#include "DHT.h"
#define DHTPIN 7 // what digital pin we're connected to
#define DHTTYPE DHT11 // DHT 11
//#define DHTTYPE DHT22 // DHT 22 (AM2302), AM2321
//#define DHTTYPE DHT21 // DHT 21 (AM2301)
DHT dht(DHTPIN, DHTTYPE);
//----wifi use
uint8_t MacData[6];
char ssid[] = "BruceSonyC5"; // your network SSID (name)
char pass[] = "12345678"; // your network password
int keyIndex = 0;
IPAddress Meip , Megateway , Mesubnet ;
String MacAddress ;
int status = WL_IDLE_STATUS;
WiFiServer server(80);
//-----end of wifi use
void setup() /*----( SETUP: RUNS ONCE )----*/
{
Serial.begin(9600);
Serial.println("DHTxx test!");
dht.begin();
if (WiFi.status() == WL_NO_SHIELD) {
Serial.println("WiFi shield not present");
// don't continue:
while (true);
}
String fv = WiFi.firmwareVersion();
if (fv != "1.1.0") {
Serial.println("Please upgrade the firmware");
}
MacAddress = GetWifiMac() ; // get MacAddress
ShowMac() ; //Show Mac Address
// attempt to connect to Wifi network:
initializeWiFi();
server.begin();
// you're connected now, so print out the status:
ShowInternetStatus();
}// END Setup
static int count = 0;
void loop()
{
// Reading temperature or humidity takes about 250 milliseconds!
// Sensor readings may also be up to 2 seconds 'old' (its a very slow sensor)
float h = dht.readHumidity();
// Read temperature as Celsius (the default)
float t = dht.readTemperature();
// Read temperature as Fahrenheit (isFahrenheit = true)
float f = dht.readTemperature(true);
Serial.print("Humidity: ");
Serial.print(h);
Serial.print(" % and ");
Serial.print("Temperature: ");
Serial.print(t);
Serial.print(" *C ");
Serial.print(f);
Serial.print(" *F\t\n");
// wifi code here
// listen for incoming clients
WiFiClient client = server.available();
if (client)
{
Serial.println("Now Someone Access WebServer");
Serial.println("new client");
// an http request ends with a blank line
boolean currentLineIsBlank = true;
while (client.connected())
{
if (client.available())
{
char c = client.read();
Serial.write(c);
// if you've gotten to the end of the line (received a newline
// character) and the line is blank, the http request has ended,
// so you can send a reply
if (c == '\n' && currentLineIsBlank)
{
// send a standard http response header
client.println("HTTP/1.1 200 OK");
client.println("Content-Type: text/html");
client.println("Connection: close"); // the connection will be closed after completion of the response
client.println("Refresh: 5"); // refresh the page automatically every 5 sec
client.println();
client.println("<!DOCTYPE HTML>");
client.println("<html>");
// output the value of each analog input pin
client.println("<head>");
client.println("<script type='text/javascript' src='https://www.gstatic.com/charts/loader.js'></script>");
client.println("<script type='text/javascript'>");
client.println("google.charts.load('current', {'packages':['gauge']});");
client.println("google.charts.setOnLoadCallback(drawChart);");
client.println(" function drawChart() {");
client.println("var data = google.visualization.arrayToDataTable([['Label', 'Value'],['hum',");
client.println(h);
client.println("],");
client.println("['Temp',");
client.println(t);
client.println("],]);");
client.println(" var options = {width: 300, height: 300,redFrom: 70, redTo: 100,yellowFrom:50, yellowTo: 70,minorTicks: 5};");
client.println("var chart = new google.visualization.Gauge(document.getElementById('chart_div'));");
client.println("chart.draw(data, options);");
client.println("}");
client.println("</script>");
client.println("</head>");
client.println("<meta charset='utf-8'>");
client.println("<body>");
client.println("<div id='chart_div' style='width: 300px; height: 300px;'></div>");
client.println("</body>");
/*
client.print("Humidity: ");
client.print(h);
client.print(" % and ");
client.print("Temperature: ");
client.print(t);
client.print("*C and ");
client.print(f);
client.print("*F (end) ");
client.println("<br />");
*/
client.println("</html>");
break;
}
if (c == '\n')
{
// you're starting a new line
currentLineIsBlank = true;
} else if (c != '\r')
{
// you've gotten a character on the current line
currentLineIsBlank = false;
}
}
}
// give the web browser time to receive the data
delay(1);
// close the connection:
client.stop();
Serial.println("client disonnected");
}
delay(800) ;
} // END Loop
void ShowMac()
{
Serial.print("MAC:");
Serial.print(MacAddress);
Serial.print("\n");
}
String GetWifiMac()
{
String tt ;
String t1, t2, t3, t4, t5, t6 ;
WiFi.status(); //this method must be used for get MAC
WiFi.macAddress(MacData);
Serial.print("Mac:");
Serial.print(MacData[0], HEX) ;
Serial.print("/");
Serial.print(MacData[1], HEX) ;
Serial.print("/");
Serial.print(MacData[2], HEX) ;
Serial.print("/");
Serial.print(MacData[3], HEX) ;
Serial.print("/");
Serial.print(MacData[4], HEX) ;
Serial.print("/");
Serial.print(MacData[5], HEX) ;
Serial.print("~");
t1 = print2HEX((int)MacData[0]);
t2 = print2HEX((int)MacData[1]);
t3 = print2HEX((int)MacData[2]);
t4 = print2HEX((int)MacData[3]);
t5 = print2HEX((int)MacData[4]);
t6 = print2HEX((int)MacData[5]);
tt = (t1 + t2 + t3 + t4 + t5 + t6) ;
Serial.print(tt);
Serial.print("\n");
return tt ;
}
String print2HEX(int number) {
String ttt ;
if (number >= 0 && number < 16)
{
ttt = String("0") + String(number, HEX);
}
else
{
ttt = String(number, HEX);
}
return ttt ;
}
void printWifiData()
{
// print your WiFi shield's IP address:
Meip = WiFi.localIP();
Serial.print("IP Address: ");
Serial.println(Meip);
Serial.print("\n");
// print your MAC address:
byte mac[6];
WiFi.macAddress(mac);
Serial.print("MAC address: ");
Serial.print(mac[5], HEX);
Serial.print(":");
Serial.print(mac[4], HEX);
Serial.print(":");
Serial.print(mac[3], HEX);
Serial.print(":");
Serial.print(mac[2], HEX);
Serial.print(":");
Serial.print(mac[1], HEX);
Serial.print(":");
Serial.println(mac[0], HEX);
// print your subnet mask:
Mesubnet = WiFi.subnetMask();
Serial.print("NetMask: ");
Serial.println(Mesubnet);
// print your gateway address:
Megateway = WiFi.gatewayIP();
Serial.print("Gateway: ");
Serial.println(Megateway);
}
void ShowInternetStatus()
{
if (WiFi.status())
{
Meip = WiFi.localIP();
Serial.print("Get IP is:");
Serial.print(Meip);
Serial.print("\n");
}
else
{
Serial.print("DisConnected:");
Serial.print("\n");
}
}
void initializeWiFi() {
while (status != WL_CONNECTED) {
Serial.print("Attempting to connect to SSID: ");
Serial.println(ssid);
// Connect to WPA/WPA2 network. Change this line if using open or WEP network:
status = WiFi.begin(ssid, pass);
// status = WiFi.begin(ssid);
// wait 10 seconds for connection:
delay(10000);
}
Serial.print("\n Success to connect AP:") ;
Serial.print(ssid) ;
Serial.print("\n") ;
}

## Slide 88: DHT11_Pin7_WIFI_Server_TwoGuage監控畫面
88
2017/6/24

## Slide 89: 使用瀏覽器進入系統
89
2017/6/24
1.先使用筆電或手機，使用wifi，並將ＷＩＦＩ熱點連接到與Ameba相同的熱點
2.進入瀏覽器(建議使用chrome)
3.網址列輸入上面IP(本例子為：http://192.168.43.150/

## Slide 90: DHT11_Pin7_WIFI_Server_TwoGuage網頁畫面
90
2017/6/24